## Slide 1: An Enabler for New E2E Transport Behaviours: More Accurate ECN Feedback Reflector (AccECN) draft-kuehlewind-tcpm-accurate-ecn-03
Bob Briscoe, BT
Richard Scheffenegger, NetApp
Mirja Kühlewind, Stuttgart Uni
IETF-90, Jul’14
Bob Briscoe’s work is part-funded by the European Community under its Seventh Framework Programme through the Reducing Internet Transport Latency (RITE) project (ICT-317700) and through the Trilogy 2 project (ICT-317756

## Slide 2: Purpose of Talk
IRTF !IETF
Introduce feedback reflector for ECN in TCP
  awesome protocol design (IMHO)
Status of AccECN in IETF
  Requirements draft finished w-g last call 21-Jul-14
Once-in-a-decade (?) chance for change
  TCP feedback meant to be generic, not just for known needs
  Once rcvr deployed, new sndr behaviours can be deployed unilaterally
  Would it meet the needs of your (research) ideas?
  Would it suit your ideas better with some tweaks?

## Slide 3: The Problem (Recap) Congestion Extent, not just Existence
Current ‘classic’ ECN feedback in TCP [RFC3168]
  if (any packet marked in RTT) {signal 1}
  else {signal 0}
<ironic> Imagine using a 128b field for 2 addresses
  if (any bit set) {address = 1}
  else {address = 0}
  </ironic>
Only ECN-for-TCP is so clunky
  TCP widely uses SACK to identify individual drops
  modern transports (DCCP, SCTCP, RTP/UDP etc) feed back extent of ECN
  need to update TCP, in its role as 1 of 2 transport protocols that work
DCTCP feedback scheme would be nice, but:
  new wire protocol but no negotiation
  greatly confused by ACK loss
  higher congestion  more ACKs
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 20 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 30 | 1
 | {0 ¦ 1} |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CE=0
CE=1
ACK every m pkts with ECE=0
ACK with ECE=1
ACK every m pkts with ECE=1
ACK with ECE=0

## Slide 4: Usefulness
Low latency queuing signals:
    Data Center TCP (DCTCP) [widely used in private networks]
      existing feedback scheme fails if ACKs dropped
    Congestion Exposure (ConEx) [IETF]
      existing TCP sufficient for drop feedback, but not for ECN
    Variable-structure congestion Control Protocol (VCP) [SIGCOMM’05]
    Chirping – TCP Rapid [Infocom’09]
    Very low threshold ECN marking [research to appear]
    Queue View (QV) [research to appear]
Allows sender to safely set CE as a test
    ECN path testing [draft-kuehlewind-tcpm-ecn-fallback]
    Receiver cheat detection [draft-moncaster-tcpm-rcv-cheat]
    Otherwise, with classic ECN, each test would conceal a whole window
0
0
1
0
1
1
1
1
0
1
1
1
0
1
1
0
0
0
0
1
Legend: ECT(0) ECT(1)
Spacing between zeros is inst. queue length

## Slide 5: Protocol Design I Where to find spare bits?
Satisfied requirements with zero extra bits
  essential part: overloaded 3 existing ECN flags in main TCP header
  supplementary part: overloaded 15b in Urgent Pointer when redundant
Non-Zero Urgent Pointer when TCP URG flag = 0?
  middlebox traversal
    seems better than for new TCP options in initial tests*
  opportunistic – not available when URG = 1
    not useful for most other protocols that need more bits
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 20 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 30 | 1
Port no’s, Seq no’s... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Offset |  |  |  | Res-erved |  |  | NS | CWR | ECE | URG | ACK | PSH | RST | SYN | FIN | Window |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Non-Urgent (if URG == 0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCP Options... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
    * Perhaps because earlier Windows versions did not zero the Urgent Pointer when URG=0
I

## Slide 6: Protocol Design II 2 complementary signals
After successful capability negotiation
cumulative counters of the 3 ECN codepoints
the sequence of ECN codepoints covered by each delayed ACK
note: packet-based not byte-based counters
note: pure ACKs are not counted
  (there are deep questions behind both these points)
III
IV
V
II

## Slide 7: Protocol Design IV Cumulative ECN Codepoint Counters
after SYN/ACK
Data receiver counts arriving CE, ECT(1) & Not-ECT (11, 01 & 00)*
Selects one counter to feed back in each ACK
  encodes in the ACE field, overloading the 3 ECN flags
  encoding fits a base 4, base 3 and base 1 counter in 3 bits!
  includes 4 most significant bits of the selected counter in the supp. field
ACE | CE (base 4) | ECT(1) (base 3) | Not-ECT (base 1)
000 | 0 |  | 
001 | 1 |  | 
010 | 2 |  | 
011 | 3 |  | 
100 |  | 0 | 
101 |  | 1 | 
110 |  | 2 | 
111 |  |  | 0
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5
 |  |  |  |  |  |  |  |  |  |  |  | Top-ACE |  |  | 
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5 | 
... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Offset |  |  |  | Res-erved |  |  | ACE |  |  | URG | ACK | PSH | RST | SYN | FIN | 
... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
  * ECT(0) found from remainder and from sequence field if available
IV

## Slide 8: Protocol Design V ECN Sequence covered by each Delayed ACK
ECN Sequence (ESQ) field
    encodes 2 Run-Lengths of SPaces, each ending in one possibly different MarK
Value of ACE selects MK2 (no need to encode in ESQ)
Receiver sends a Delayed ACK on any of these events:
    Max delayed ACK coverage is reached (e.g. 2 full-sized segments)
    Delayed ACK timer expires (e.g. 500ms)
    Pattern becomes too complex to encode
in one ACK, it is possible to encode a sequence of:
    up to 15 segments for typical marking patterns Examples
    3 segments for any possible marking pattern
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5
 |  | RL1 |  |  | RL2 |  |  | SP |  | MK1 |  |  |  |  | 
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5
 |  | ESQ |  |  |  |  |  |  |  |  |  | Top-ACE |  |  | 
RL1 = 5
RL2 = 2
MK1
MK2
next RL1
VI
V

## Slide 9: Protocol Design VI ECN Sequence covered by each Delayed ACK
SPace or MarK1 can be any of:
N: Not-ECT (00) 0: ECT(0) (10) 1: ECT(1) (01) C: CE (11)
Examples
1 0 0 0 0 C 0 0 0 0 0
0 0 C C C
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
C 0 0 0 0 C
N N
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 |  | 
 |  | RL1 |  |  | RL2 |  |  | SP |  | MK1 |  |  | 
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5
 |  | ESQ |  |  |  |  |  |  |  |  |  | Top-ACE |  |  | 
 |  | 6 | 4 | 0 | C | 
 |  | 1 | 
 |  | 4 | 0 | C | 0 | 
 |  | 0 | 
 |  | 7 | 7 | 0 | 0 | 
 |  | 0 | 
 |  | 1 | 4 | 0 | C | 
 |  | C | 
 |  | 0 | 1 | N | [0] | 
 |  | N | 
 | ACE | 
VI

## Slide 10: AccECN Protocol Features Summary
Requirement | Classic ECN | ECN Nonce | DCTCP | AccECN Urg-Ptr | AccECN TCP opt | AccECN essential
Resilience | + | + | - | + | + | o
Timeliness | o | o | - | + | + | +
Integrity | - | o | - | +* | +* | +*
Accuracy | - | - | - | + | + | +
Ordering | - | - | + | + | + | -
Complexity | ++ | + | o | - | - | o
Overhead | ++ | o | o | + | o | ++
Compatibility | o | o | - | o | - | o
* = compatible with an independent zero-overhead integrity solution

## Slide 11: Open Design Issues
Could simplify by removing sequence (ESQ) feedback entirely?
  Instead require the receiver to disable delayed ACKs?
    during slow-start (Linux receiver does this heuristically)?
    requested by the sender?
  But, is ACKing every segment acceptable?
if supp. field unavailable, certain counter(s) could rarely be seen
  if they are rarely last in a delayed ACK (maybe due to unfortunate synch.)
See Appendix C of draft, for these and 7 other more detailed issues
 |  | ESQ | Top-ACE
x?

## Slide 12: Alternative Design Choices
Roughly highest importance first
Earlier ECN feedback (on SYN/ACK)
Remote Delayed ACK Control
Earlier ECN fall-back (on SYN/ACK)
Shave 1 bit off ECN sequence field
See Appendix B of draft
where to draw the line?
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5
 | DAC | ESQ |  |  |  |  |  |  |  |  |  | Top-ACE |  |  | 

## Slide 13: summary & next steps
awesome protocol design (IMHO)
  zero (extra) header bits
still room for improvement
  pls ponder design alternatives & issues (Appendices B & C)
  simple enough for high performance?
  generic enough for your research ideas?
Requirement | AccECN Urg-Ptr
Resilience | +
Timeliness | +
Integrity | +
Accuracy | +
Ordering | +
Complexity | -
Overhead | +
Compatibility | o

## Slide 14: An Enabler for New E2E Transport Behaviours: More Accurate ECN Feedback Reflector (AccECN) Requirements draft-ietf-tcpm-accecn-reqs-06 Proposed Protocol Spec draft-kuehlewind-tcpm-accurate-ecn-03
Q&A
spare slides

## Slide 15: Protocol Design III Capability Negotiation
AccECN is a change to TCP wire protocol
    only to be used if both ends support it
client negotiates support on initial SYN
    using the 3 ECN-related TCP flags
    server sets the 3 flags accordingly on the SYN/ACK
      or it replies as the latest variant it recognises
    if nec. client downgrades to match the server
supp. field not used until 3rd leg of handshake
    consumes no TCP option space on SYN
    if at any time supp. field = 0  middlebox interference
SYN |  |  |  | 
 | NS =1 | CWR=1 | ECE=1 | 
SYN/ACK |  |  |  | 
 | NS =0 | CWR=1 | ECE=0 | 
III

## Slide 16: Opportunistic but not Presumptuous?
Presumptuous to reassign Urgent Pointer experimentally?
While experimental:
    use a TCP option for the supplementary part
    Reserved 15b in Urgent Pointer
      to use if this progresses to standards track
    Experimental implementations required to recognise either location
AccECN still ‘works’ if TCP option is cleared or discarded
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 20 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 30 | 1
Port no’s, Seq no’s... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Offset |  |  |  | Res-erved |  |  | NS | CWR | ECE | URG | ACK | PSH | RST | SYN | FIN | Window |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Urgent Pointer |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCP Options... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Kind = 0xKK |  |  |  |  |  |  |  | Length = 4 |  |  |  |  |  |  |  | Supplementary AccECN |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCP Options... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 17: Interaction with other TCP variants
Server can use AccECN with SYN Cookies
    capability negotiation can be inferred
AccECN compatible with main TCP options:
    Max Segment Size (MSS)
    Timestamp
    Window Scaling
    Selective ACKs (SACK)
    Authentication Option (TCP-AO)
    TCP Fast Open (TFO)
    Multipath TCP (MPTCP)
AccECN consumes no option space on the SYN
  even when deployed experimentally as a TCP option

## Slide 18: Protocol Features detailed explanations
Resilience
    DCTCP confused by ACK loss
Timeliness
    Classic ECN: only timely once per RTT
    DCTCP is always 1 transition behind
Integrity
    ECN nonce: relies on receiver incriminating itself
    DCTCP & AccECN compatible with approach in draft-moncaster-tcpm-rcv-cheat
Accuracy
    DCTCP lack of resilience impacts accuracy
Ordering
    ‘AccECN essential’ is the fall-back when a middlebox clears the sequence field
Complexity
    Hard to quantify
Overhead
    ECN Nonce marked down because it consumes the last ECN-IP codepoint
    AccECN Urg-Ptr marked down because it prevents others using the Urgent Pointer
Compatibility
    Class ECN has had continuing problems with middlebox traversal
    DCTCP is unsafe to interoperate with other TCP variants
    ‘AccECN Urg-Ptr’ seems good at traversal, but more experiments needed
    ‘AccECN TCP opt’ unlikely to traverse middleboxes that wipe TCP options
Requirement | Classic ECN | ECN Nonce | DC TCP | AccECN Urg-Ptr | AccECN TCP opt | AccECN essential
Resilience | + | + | - | + | + | o
Timeliness | o | o | - | + | + | +
Integrity | - | o | +* | +* | +* | +*
Accuracy | - | - | - | + | + | +
Ordering | - | - | + | + | + | -
Complexity | ++ | + | o | - | - | o
Overhead | ++ | o | o | + | o | ++
Compatibility | o | o | - | o | - | o