## Slide 1: Echo Cookie TCP Option
Bob Briscoe
Nov 2014
Bob Briscoe’s work is part-funded by the European Community under its Seventh Framework Programme through the Trilogy 2 project (ICT-317756)

## Slide 2: status
draft-briscoe-tcpm-echo-cookie-00
  initial individual draft
arose from SYN-option-space extension work, but orthogonal
separated out as focused draft
  all SYN-option-space-extensions need something like this
  replaces tcpcrypt SYNCOOKIE/ACKCOOKIE suboptions

## Slide 3: Problem
SYN flood
  exhausts TCP server’s pending connection state
  while SYN/ACK checks validity of source address
SYN cookie,.. and friends
  store server connection state in flight not in memory
  still needed (despite some thinking server config is sufficient)
  but... further problem
15 bits of cookie space
  embedded in 16b initial seq no (ISN) and 9 lowest significant bits of timestamp (if supported)
  only enough for degraded max seg size, wnd scale & SACK-ok
  plus some scope for server to infer other options it negotiated
with more, larger options on SYN: not enough space
  with SYN-extension: really not enough space
SYN flood becomes either connection state or option denial attack
S
C
S
S

## Slide 4: Echo Cookie TCP Option
  underlying the space problem:
  SYN cookie limited to fields that all TCP clients echo (ISN, TS)
solution: a larger cookie jar
  mandatory to implement with any new TCP option
  and mandatory with extra SYN option space
  ie. other options implicitly signal client support for EchoCookie
the EchoCookie option
  if host receives a cookie, it MUST reflect it back
  sender can choose size and contents
client MAY include 2-octet EchoCookie flag option on SYN
  e.g. when using options that do not signal implicit support
EchoCookie | Len=X (X>1) | Cookie
1B | 1B | (X-2)B

## Slide 5: security considerations (discuss on list pls)
if client negotiated state using a secured protocol
  cookie MUST be echoed with at least as strong security
could be used as a reflection attack?
  SYN/ACK MUST NOT exceed size of SYN
  no need to include data in SYN within cookie
    server not ACKing the data causes a retransmit anyway
    TFO cookie serves as proof the source address is valid
    server can/SHOULD rate-limit to repeated and/or unresponsive source IPs?
server SHOULD only use when under stress?
mechanism server uses to verify returned cookie?
  no need to standardise?
any other new attack vectors?

## Slide 6: next steps
security discussion pls
applicability:
  solely SYN/ACK – ACK?
  solely server-client-server?
  any segment?
intended status: proposed std?
adoption?