## Slide 1: Inner Space
Bob Briscoe
Oct 2014
draft-briscoe-tcpm-inner-space-01

## Slide 2: menu
Status & purpose of presentation
Inner Space protocol
Benefits & drawbacks
Tricky bits
Extensions (in spare slides)
Applicability / compatibility
Opportunities / further work
Next steps

## Slide 3: purpose & status
problem
  hard to extend TCP
    only 40B for options
    middleboxes only forward their stereotype of TCP
purpose of this talk
  introduce proposed solution
  motivate forward thinking (and critical review)
status
  Extensive Internet Draft posted to IETF TCP mtce & minor mods WG
    draft-briscoe-tcpm-syn-op-sis -00,01,02 -> draft-briscoe-tcpm-inner-space-00,-01
    5 revisions since Jul IETF, individual draft – no IETF status (yet)
    triggered by “more space on a SYN is impossible” in Joe Touch’s EDO proposal for extra space on non-SYN only (adopted)
    counter proposal to my other 2 proposals with Joe Touch (also individual status)
    lots of list discussion

## Slide 4: encapsulation model
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload

## Slide 5: TCP segment structure (SYN=0)
Sent payload size (SPS) | Inner Options Offset (InOO) | Len
16b | 14b | 2b
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
Not to scale
All offsets in 4-octet word units, except SPS is in octets
Base TCP header
Outer Options
TCP Payload
Data Offset (DO)
IP Payload Size
Before
After (SYN=0)
InSpace solely contains frame size info

## Slide 6: TCP segment structure
presence of Inspace flagged by magic no. at start of each stream
avoided an Outer TCP Option as the flag, which could be stripped
inherently safe to flag within the payload – shares fate with options
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=0
TCP Data

## Slide 7: TCP byte-stream
robust to resegmentation
Inner Options not prone to stripping
reliable ordered delivery of Inner Options
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
TCP
TCP
Control
Data

## Slide 8: dual handshake... and migration to single
different source ports, same dest. port
no co-ordination needed between server threads
  can be physically separate replicas
Can use single SYN-U handshake
  when server is in cached white-list
  once deployment is widespread (no need for white-list)
  Fall-back to SYN if no SYN-ACK-U
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U
SYN-ACK
SYN-ACK
SYN
RST
ACK
SYN-U
SYN-ACK
SYN-ACK-U
SYN
ACK
RST
-U = upgraded, i.e. magic no. at start of TCP Data
1
2
2
Cont...
Cont...
Upgraded Client
Upgraded Server
SYN-U
SYN-ACK-U
ACK
Cont...
1
3

## Slide 9: middlebox domination strategy
non-goal
evasion of security middleboxes
  they will evolve to check Inner Options
goal
Inner Space deployed for something useful (e.g. tcpcrypt)
  traverses most middleboxes, so reaches critical mass
  can deploy integrity protection over TCP Data
  (cannot protect Outer Options today – would fail too often)
raises stakes
  then tampering with Inner Options will break comms, not just the theoretical potential benefit of a new option
puts security middlebox designers on the back foot
  blocking comms just ‘cos options are non-typical will not sell
  distinguishing attacks from the latest advances will sell
result
mess with my options and you shoot yourself in the foot

## Slide 10:  benefits
no arbitary limit on option space
incremental deployment both of Inner Space itself and of new options it enables
  middlebox traversal
  legacy server fall-back
no extra handshaking delay
reliable ordered delivery of control options

## Slide 11:  drawbacks - overheads
Dual Handshake Example
  Latency (Upgraded Server) Zero (Legacy Server) Worst of 2
  Connection Rate P*D 8%
  Connection State P*D/R 2.7%
  Network Traffic 2*H*P*D/J counting in bytes 0.03%
  2*P*D/K counting in packets 0.2%
  Processing {? pending implementation}
Option on every non-empty segment
  Network Traffic P*Q*4/F 0.04%
  Processing {? pending implementation}
P : [0-100%] proportion of connections that use extra option space 80%
D : [0-100%] proportion of these that use dual handshake 10%
R : [round trips] ave. hold time of connection state 3
H : 88B for IPv4 or 108B for IPv6 (see draft for assumptions)
J : ave bytes per connection (in both directions) 50KiB
K : ave packets per connection (in both directions) 70 packets
Q : ave prop’n of InSpace connections that use it after handshake 10%
F : [B] ave frame size 750B

## Slide 12:  drawbacks - non-deterministic
the magic number approach traverses option stripping middleboxes, but...
probability that an Upgraded SYN or SYN/ACK is mistaken for an Ordinary Segment: Zero
probability that an Ordinary SYN or SYN/ACK with zero payload is mistaken for an Upgraded Segment: Zero
probability that payload data in an Ordinary SYN or SYN/ACK is mistaken for an Upgraded Segment: << 2-66 (roughly 1 connection collision globally every 40 years)

## Slide 13: tricky bits - zero payload segments
zero payload segments
  MAY include an Inner Option
  SHOULD NOT repeat the same Inner Options until more payload
other tricky bits  spare slides or draft
  option processing order
  options that alter byte-stream
    e.g. encrypt or compress
  the EchoCookie for SYN floods
  retransmissions during handshake
Without the ‘SHOULD NOT’ it would continue to ACK ACKs for ever

## Slide 14: disabling Inner Space temporarily
set Sent Payload Size (SPS) to special max value 0xFFFF
  sent segment was not 0xFFFF octets, but behave as if it was
  values above 0xFFE8 (= 216 – 25) are usable but not believable
regularly repeat just the 4B InSpace option
  every 0xFFFF octets (=44.7 * 1466B typical full-sized segments)
could disable Inner Space for rest of connection
  separate ModeSwitch TCP option – see spare slide or draft

## Slide 15: Extensions – summary of dependencies
mandatory if implement Inner Space
  EchoCookie TCP option
extensions: optional while Inner Space is Experimental
    ModeSwitch TCP Option (scope wider than Inner Space)
    Explicit Dual Handshake (2 Outer TCP Options)
    Jumbo InSpace Option
    Inner Space segment structure for DPI traversal
DPI
see spare slides or draft

## Slide 16: applicability & compatibility (interim*)
have to use Outer Option
  typically concerned with individual segments
    Subsequent Timestamps
    Selective ACK (SACK)
    Multipath TCP Data ACK (in Data Sequence Signal – DSS)
best as Inner Option
  typically concerned data as a stream
    tcpcrypt CRYPT
either Inner or Outer Option
  typically starting the connection (and therefore a segment)
    (4B) Max Segment Size (MSS)
    (2B) SACK-ok
    (3B) Window Scale (WS)
    (10B) First timestamp (TS)
    (16B) TCP Authentication Option
    (6-18B) TCP Fast Open (TFO)
    tcpcrypt MAC
    (12B) MPTCP except Data ACK
* Many of the above schemes involve multiple different types of TCP option, which need to be separately assessed.

## Slide 17: Inner Space & TCP Fast Open (TFO)
If Upgraded Client uses TFO
  MUST place cookie in Inner of SYN-U
  then Legacy Server will not pass corrupt TCP Data to app before RST
If dual h/s, Upgraded Server will pass payload to app twice
  OK, because TFO only applicable if app immune to duplication
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U +InnerTFO
SYN-ACK
SYN-ACK
SYN+OuterTFO
RST
ACK
SYN-U +InnerTFO
SYN-ACK-U
SYN+OuterTFO
ACK
RST
-U = upgraded, i.e. magic no. etc. at start of TCP Data
SYN-ACK
App
App
1
2

## Slide 18: Inner Space & tcpcrypt
tcpcrypt capability negotiation currently adds a round trip
  not viable to add 1RTT delay to every connection to introduce opportunistic encryption
tcpcrypt currently attempts most of Inner Space
  in various complicated bespoke ways
  have proposed how to structure tcpcrypt over Inner Space
  cuts 1.5 rounds  makes tcpcrypt viable
  cuts out two states – greatly simplifies
  (?) decouples tcpcrypt from TCP state m/c
  tcpcrypt can encrypt Inner Options (incl. its own)
    because that needs reliable ordered delivery

## Slide 19: Inner Space & MPTCP
MPTCP adds Data ACK (in the DSS TCP Option)
  cumulative ACK of the set of sub-flows cannot be inferred
Data ACK is a per-segment message
  cannot use Inner Options
    would not be interpretable on reception (if out of order)
    potential deadlock: must not require receive buffer to ACK [1]
Three ways forward
  give up – leave all MPTCP TCP Options as Outer Options
  use Inner Space for a low latency MPTCP, except DSS and a way to test path for stripping DSS
  extend Inner Space to include Outer Options within TCP Data without using RWND or sequence space (hard – see next)
[1] Raiciu et al “How Hard Can It Be? Designing and Implementing a Deployable Multipath TCP”

## Slide 20: opportunities / further work
tcpcrypt-v2 decomposition
probes
  any Inner Options delivered reliably in order
relation to Minion, and multi-stream protocols
Outer Options in Inner for middlebox traversal
    without consuming rwnd (cf. fixed space for Outer Options)
    without consuming sequence space (avoiding middlebox ‘correction’)
    delivered immediately in received order, not sent order

## Slide 21: next steps
adoption: IETF TCP mtce & minor mod’s
  comparison with other proposals
  converge on stable design ASAP
review focus
  critique, e.g. design for performance
  mandatory/optional elements
path testing
  is DPI bypass necessary? viable?
implementation
  compatibility testing
IAB workshop on stack evolution in a middlebox Internet

## Slide 23: tricky bits – option processing order
only on the first segment of each half-connection
  on later segments, Outer Options have to be processed before Inner
  reason: can’t find Inner Options if still waiting to fill a sequence gap
Base TCP header
Outer Options
InSpace Option
Prefix Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
SPS | InOO | Len
Magic Number B | SOO | CU
16b | 14b | 2b
Suffix Options Offset (SOO)
Suffix Options
Inner Options

## Slide 24: tricky bits – processing order: one level of recursion
If TCP alters the TCP Data (e.g. decrypt, decompress in the receiving case, for example)
  SYN=1: if it hasn’t previously found MagicA, it looks again
  SYN=0: There might be a rekey command in an encrypted Inner Option. So the TCP receiver decrypts up to the end of each set of Inner Options, processes those options, then continues decrypting (which might be with a new key).

## Slide 25: tricky bits – SYN floods
current SYN cookie mechanism is too small for the ambition to use lots of options
  because it packs the cookie into part of the Initial Seq No
  solution: a larger cookie jar that an Inner Space host MUST implement
the EchoCookie option (can be independent of Inner Space)
  if host receives a cookie, it MUST reflect it back
  sender can choose size and contents
other opportunities
  tcpcrypt could use this
EchoCookie | Len=X (X>1) | Cookie
1B | 1B | (X-2)B

## Slide 26: extension - ModeSwitch
would be nice to be able to turn off Inner Space protocol
  each ends need to know when the other end has switched
  to co-ordinate which will be the last InSpace options
introduced a generic ModeSwitch Inner TCP option
  rather than embed an ‘off switch’ into the InSpace option
    R : Request mode (special) I : Inner Space mode CU : currently unused space for yet-to-be-defined TCP modes
ModeSwitch | Len=3 | CU | I | R
1B | 1B | 1B |  | 
I=0,R=1
I=0,R=0
I=0,R=0
default: I=1
data
pure ACKs

## Slide 27: why switching connection mode is tricky
C
InSpace
A
TCP Payload
InSpace
B
TCP Payload
InSpace
C
InSpace
D
InSpace
E
A
TCP Payload
B
TCP Payload
D
E
drop
Inner Options: reliable, ordered
Outer Options: not
rekey TCP-AO with Header Authentication
rekey TCP-AO with Header Authentication
(common) case of no data in one direction for a while
TCP-AO added bespoke solution: lists operative keys in every header then switches key back and forth during out of order headers
control
data
control
data

## Slide 28: extension – DPI traversal
conjecture: DPI often parses payload & stops when it finds what it needs
solution?: locate MagicA at the end of the segment
  server searches for MagicA at end if not at start
can’t work from the end of every segment, only the first
  then use the spare first SPS (SPS#1) for the second segment
Base TCP header
Outer Options
SYN=1
InSpace Option#1
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Magic A
1
Base TCP header
Outer Options
InSpace Option#2
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
SPS#2
first SYN=0
TCP Payload
SPS#1
DPI

## Slide 29: spare slides - to write
handshake retransmissions
explicit dual handshake
  corner cases of dual handshake
  deferred data in SYN