## Slide 1: Inner Space for tcpinc
Bob Briscoe
Nov 2014
draft-briscoe-tcpm-inner-space-01
Bob Briscoe's work is part-funded by the European Community under its Seventh Framework Programme through the Trilogy 2 (ICT-317756) and the RITE (ICT-317700) projects

## Slide 2: opportunistic encryption
tcpinc depends on TCP options
TCP options are changing...
  special session in tcpm on 4 drafts
No handshake latency
Middlebox not a downgrade
How? Inner Space protocol
Authentication coverage insights
IPsec
SSL
TLS
unencrypted
Reminder: Project Goal
IPsec
SSL
TLS
opportunistic
TCP traffic today
Goal for TCP traffic
unencrypted

## Slide 3: opportunistic delay
IPsec
SSL
TLS
unencrypted
Reminder: Project Goal
IPsec
SSL
TLS
opportunistic
TCP traffic today
Goal for TCP traffic
unencrypted
IPsec
SSL
TLS
unencrypted
Result
opportunistic
Ave. Alexa 1000 Web page
44 TCP connections*
  from 15 servers†
* as of Nov 2014
† as of early 2013
httparchive.org

## Slide 4: tcpcrypt latency & Inner Space session initialisation
cuts out two states
decouples tcpcrypt from TCP state machine?
SYN
SYN-ACK
ACK
tcpcrypt 2 RTT
tcpcrypt.v2 1 RTT
time
without
with Inner Space
client data first
Legend: loop groups messages that can be sent in the same packet
`
cleartext ciphertext
TCP header
TCP options
App data
Hello
PKCONF
INIT1
ACK
INIT2
App data
SYN
SYN-ACK
INIT1+
INIT2+
(App data)
ACK
App data
tcpcrypt.v2 0.5 RTT
INIT1, sym-cipher-list, N_C, pub-cipher, PK_C
INIT2, sym-cipher, KX_S
INIT1+, pub-cipher-list, sym-cipher-list, N_C, PK_C
INIT2+, sym-cipher, KX_S; MAC<m>
server data first
MAC
MAC

## Slide 5: tcpcrypt latency with Inner Space session resume
see [Briscoe14] for details
SYN
SYN-ACK
ACK
tcpcrypt.v2 0 RTT
time
without
with Inner Space
client data first
NEXTK1
NEXTK2
App data
SYN
SYN-ACK
TFO
MAC
tcpcrypt 1 RTT
MAC
App data
NEXTK2
App data
NEXTK1
(TFO)
MAC
Legend: loop groups messages that can be sent in the same packet
`
cleartext ciphertext
TCP header
TCP options
App data
MAC
App data
NEXTK2

## Slide 6: middleboxes: detect-and-downgrade? not good enough
tcpinc (tcpcrypt and TCP-TLS) relies on new TCP options
  so tcpinc would disable itself on ~10% of paths
  when middlebox downgrade of tcpinc is so unremarkable it makes a downgrade attack indistinguishable from a middlebox
    <large_agency> can snoop on anyone
[Honda11]
unknown TCP option stripped | 
to port | % paths
80 (HTTP) | 14%
443 (HTTPS) | 6%
34343 (unassigned) | 4%

## Slide 7: middlebox domination strategy
long term aim
authenticate options
if turned on option authentication today
  ~10% of connections would break
  the ends break a working service
middlebox domination strategy
  Inner Space + option authentication (breaks 0%)
then, if middleboxes move into the TCP data
  the middleboxes break a working service
if you want to shoot them,
why shoot yourself in the foot
when you can make them shoot themselves in the foot?

## Slide 8: Inner Space – TCP segment structure (SYN=0)
Sent payload size (SPS) | Inner Options Offset (InOO) | Len
16b | 14b | 2b
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
Not to scale
All offsets in 4-octet word units, except SPS is in octets
Base TCP header
Outer Options
TCP Payload
Data Offset (DO)
IP Payload Size
Before
After (SYN=0)
InSpace is solely a framing header

## Slide 9: Inner Space – TCP segment structure
presence of Inspace flagged by magic no. at start of each stream
avoided an Outer TCP Option as the flag, which could be stripped
inherently safe to flag within the payload – shares fate with options
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=0
TCP Data

## Slide 10: Inner Space – TCP byte-stream
robust to resegmentation
Inner Options not prone to stripping
reliable ordered delivery of Inner Options
  makes rekey easy (gives tcpcrypt TLS-like records)
  tcpinc can encrypt Inner Options (incl. its own)
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
Control
Data
Sent
Received

## Slide 11: rekey message on an unreliable unordered segment
C
problematic if key applies to headers
InSpace
A
TCP Payload
InSpace
B
TCP Payload
InSpace
C
InSpace
D
InSpace
E
A
TCP Payload
B
TCP Payload
D
E
drop
Inner Options: reliable, ordered
Outer Options: not
rekey
rekey
(common) case of no data in one direction for a while
TCP-AO added bespoke solution: lists operative keys in every header then switches key back and forth during out of order headers
control
data
control
data

## Slide 12: transformation of the datastream controlled by TCP options within the datastream
e.g. (de)crypt, (de)compress
care with processing order: recursion limited to one level
  SYN=1:
    if not previously found MagicA, retry after transformation
  SYN=0:
    (de)crypt progressively
    up to the end of each set of Inner Options
    process those options
    then continue with next segment (might be with a new key)

## Slide 13: transformation of the datastream controlled by TCP options within the datastream
e.g. (de)crypt, (de)compress
care with processing order: recursion limited to one level
  SYN=1:
    if not previously found MagicA, retry after transformation
  SYN=0:
    (de)crypt progressively
    up to the end of each set of Inner Options
    process those options
    then continue with next segment (might be with a new key)

## Slide 14: message authentication coverage
coverage options [Marcelo BB]:
  payload only
  payload plus some header fields
    MAC in a TCP option
    MAC in the payload
      possible exception: MAC for pure ACKs in TCP option
    MAC for header in a TCP option; and for payload in payload
    MAC in a TCP option... in the payload
Inner Space preserves the 1-1 mapping between
  MAC, payload & Inner TCP options of each segment
  but not Outer Options and not the main TCP header (next slide)
gotcha: MAC consumes sequence space on pure ACK
  could write ad hoc rules, e.g. "defer ACK if no payload"
  full solution (next revision): unreliable & reliable Inner Options
InSpace Option
Inner Options
TCP Payload
TCP Payload
MAC

## Slide 15: message authentication of the main TCP header
middlebox transformations
    NAT
    resegmentation
    Seq No Shift
    ACK thinning
    <more will be discovered>
not really attacks, but naive authentication would fail
  approach so far: absolve these headers from authentication
a feasible approach (not universally applicable)
  using inner options, sender reveals the original* once per connection
  rcvr reverses shifts, reconstructs sent (pseudo)segments
  rcvr verifies sent MAC against reconstructed pseudosegments
summary: verify that header transformations are consistent
* privacy concern?

## Slide 16: Inner Space – encapsulation model
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload

## Slide 17: Inner Space – applicability & compatibility1,2
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload
re: segment delivery
Timestamps
SACK
MPTCP Data ACK
MAC (if covers header)
re: stream delivery
tcpcrypt CRYPT
re: connection
Max Segt Size
SACK-ok
Wnd Scale
Timestamp (1st)
TCP-AO
TCP Fast Open
MPTCP (excl. DACK)
tcpcrypt MAC
TCP-TLS
1 Many of the above schemes involve multiple different types of TCP option, see draft.
2 Next revision supports all options as Inner
re: connection
Max Segt Size
SACK-ok
Wnd Scale
Timestamp (1st)
TCP-AO
TCP Fast Open
MPTCP (excl. DACK)
tcpcrypt MAC
TCP-TLS

## Slide 18: summary
much more TCP option space
cuts handshake latency ...as a service
middlebox traversal ...as a service
sent segment reconstruction ...as a service
reliable ordered options ...as a service
next steps
mismatch in maturity?
  tcpm chairs: "no hurry"
tcpcrypt.v2 decomposition
  review pls
path testing
  data in SYN, is DPI bypass necessary? viable?
implementation
  compatibility testing
IAB workshop on stack evolution in a middlebox Internet
  principles
TCP
TCP

## Slide 20: contents
No handshake latency
Middlebox not a downgrade
How? Inner Space protocol
Authentication coverage insights
Spare slides
More info
Dual handshake
Overhead
Extensions – DPI traversal, EchoCookie
Tricky bits
Interaction with TCP Fast Open
Work in progress

## Slide 21: more info
Inner Space for TCP Options
  draft-briscoe-tcpm-inner-space
[Bagnulo14] Protect or not the TCP header fields
  http://www.ietf.org/mail-archive/web/tcpinc/current/msg00359.html
[Briscoe14] tcpcrypt decomposition:
  http://www.ietf.org/mail-archive/web/tcpinc/current/msg00384.html
[Honda11]
  Honda, M., Nishida, Y., Raiciu, C., Greenhalgh, A., Handley, M., and H. Tokuda, "Is it Still Possible to Extend TCP?", Proc. ACM Internet Measurement Conference (IMC'11) 181--192, November 2011.

## Slide 22: dual handshake... and migration to single
different source ports, same dest. port
no co-ordination needed between server threads
  can be physically separate replicas
Can use single SYN-U handshake
  when server is in cached white-list
  once deployment is widespread (no need for white-list)
  Fall-back to SYN if no SYN-ACK-U
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U
SYN-ACK
SYN-ACK
SYN
RST
ACK
SYN-U
SYN-ACK
SYN-ACK-U
SYN
ACK
RST
-U = upgraded, i.e. magic no. at start of TCP Data
1
2
2
Cont...
Cont...
Upgraded Client
Upgraded Server
SYN-U
SYN-ACK-U
ACK
Cont...
1
3

## Slide 23:  drawbacks - overheads
Dual Handshake Example
  Latency (Upgraded Server) Zero (Legacy Server) Worst of 2
  Connection Rate P*D 8%
  Connection State P*D/R 2.7%
  Network Traffic 2*H*P*D/J counting in bytes 0.03%
  2*P*D/K counting in packets 0.2%
  Processing {pending implementation} ?
Option on every non-empty segment
  Network Traffic P*Q*4/F 0.04%
  Processing {pending implementation} ?
Example
P : [0-100%] proportion of connections that use extra option space 80%
D : [0-100%] proportion of these that use dual handshake 10%
R : [round trips] ave. hold time of connection state 3
H : 88B for IPv4 or 108B for IPv6 (see draft for assumptions)
J : ave bytes per connection (in both directions) 50KiB
K : ave packets per connection (in both directions) 70 packets
Q : ave prop'n of InSpace connections that use it after handshake 10%
F : [B] ave frame size 750B

## Slide 24:  drawbacks - non-deterministic
the magic number approach traverses option stripping middleboxes, but...
probability that an Upgraded SYN or SYN/ACK is mistaken for an Ordinary Segment: Zero
probability that an Ordinary SYN or SYN/ACK with zero payload is mistaken for an Upgraded Segment: Zero
probability that payload data in an Ordinary SYN or SYN/ACK is mistaken for an Upgraded Segment: << 2-66 (roughly 1 connection collision globally every 40 years)

## Slide 25: Extensions – summary of dependencies
mandatory if implement Inner Space
  EchoCookie TCP option
extensions: optional while Inner Space is Experimental
    ModeSwitch TCP Option (scope wider than Inner Space)
    Explicit Dual Handshake (2 Outer TCP Options)
    Jumbo InSpace Option
    Inner Space segment structure for DPI traversal
DPI
see spare slides or draft

## Slide 26: tricky bits – SYN floods
current SYN cookie mechanism is too small for the ambition to use lots of options
  because it packs the cookie into part of the Initial Seq No
  solution: a larger cookie jar that an Inner Space host MUST implement
the EchoCookie option (can be independent of Inner Space)
  if host receives a cookie, it MUST reflect it back
  sender can choose size and contents
other opportunities
  tcpcrypt could use this
EchoCookie | Len=X (X>1) | Cookie
1B | 1B | (X-2)B

## Slide 27: extension – DPI traversal
conjecture: DPI often parses payload & stops when it finds what it needs
solution?: locate MagicA at the end of the segment
  server searches for MagicA at end if not at start
can't work from the end of every segment, only the first
  then use the spare first SPS (SPS#1) for the second segment
Base TCP header
Outer Options
SYN=1
InSpace Option#1
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Magic A
1
Base TCP header
Outer Options
InSpace Option#2
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
SPS#2
first SYN=0
TCP Payload
SPS#1
DPI

## Slide 28: tricky bits - zero payload segments
zero payload segments
  MAY include an Inner Option
  SHOULD NOT repeat the same Inner Options until more payload
other tricky bits  spare slides or draft
  the EchoCookie for SYN floods
  retransmissions during handshake
  explicit dual handshake
    corner cases of dual handshake
    deferred data in SYN
Without the 'SHOULD NOT' it would continue to ACK ACKs for ever

## Slide 29: tricky bits – option processing order
only on the first segment of each half-connection
  on later segments, Outer Options have to be processed before Inner
  reason: can't find Inner Options if still waiting to fill a sequence gap
Base TCP header
Outer Options
InSpace Option
Prefix Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
SPS | InOO | Len
Magic Number B | SOO | CU
16b | 14b | 2b
Suffix Options Offset (SOO)
Suffix Options
Inner Options

## Slide 30: Inner Space & TCP Fast Open (TFO)
If Upgraded Client uses TFO
  MUST place cookie in Inner of SYN-U
  then Legacy Server will not pass corrupt TCP Data to app before RST
If dual h/s, Upgraded Server will pass payload to app twice
  OK, because TFO only applicable if app immune to duplication
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U +InnerTFO
SYN-ACK
SYN-ACK
SYN+OuterTFO
RST
ACK
SYN-U +InnerTFO
SYN-ACK-U
SYN+OuterTFO
ACK
RST
-U = upgraded, i.e. magic no. etc. at start of TCP Data
SYN-ACK
App
App
1
2

## Slide 31: work in progress
Unreliable as well as reliable ordered Inner Options
    without consuming rwnd
    without consuming sequence space (avoiding middlebox 'correction')
    delivered immediately in received order, not sent order
    based on ideas in TCP Minion
    spec fully written-up – internal review prior to posting