## Slide 1: Inner Space
Bob Briscoe
Nov 2014
draft-briscoe-tcpm-inner-space-01
Bob Briscoe’s work is part-funded by the European Community under its Seventh Framework Programme through the Trilogy 2 (ICT-317756) and the RITE (ICT-317700) projects

## Slide 2: problem (Inner Space addresses all these)
no arbitrary limit to TCP option space on all segments
  SYN, SYN/ACK, non-SYN
middlebox traversal
  not just detect-and-die
  traverse resegmentation, option-stripping, DPI Web filters etc.
  for itself and for all TCP options it supports
legacy server fall-back with no added latency
make TCP options easy
  they will just work
  from the SYN onwards

## Slide 3: middleboxes: detect-and-die?
[Honda11]
to port | % paths stripped
80 (HTTP) | 14%
443 (HTTPS) | 6%
34343 (unassigned) | 4%
EDO
  if stripped from SYN or SYN/ACK: disable EDO
  required on all segments, even if space not needed
  if stripped mid-connection, ignore segment
tcpcrypt + EDO
  tcpcrypt will disable itself on ~10% of paths
  downgrade as the norm
  N?A can snoop on anyone
option stripper

## Slide 4: Inner Space – TCP segment structure (SYN=0)
Sent payload size (SPS) | Inner Options Offset (InOO) | Len
16b | 14b | 2b
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
Not to scale
All offsets in 4-octet word units, except SPS is in octets
Base TCP header
Outer Options
TCP Payload
Data Offset (DO)
IP Payload Size
Before
After (SYN=0)
InSpace solely contains frame size info

## Slide 5: Inner Space – TCP segment structure
presence of Inspace flagged by magic no. at start of each stream
avoided an Outer TCP Option as the flag, which could be stripped
inherently safe to flag within the payload – shares fate with options
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
Base TCP header
Outer Options
InSpace Option
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=0
TCP Data

## Slide 6: Inner Space – TCP byte-stream
robust to resegmentation
Inner Options not prone to stripping
reliable ordered delivery of Inner Options
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
TCP
TCP
Control
Data

## Slide 7: dual handshake... and migration to single
different source ports, same dest. port
no co-ordination needed between server threads
  can be physically separate replicas
Can use single SYN-U handshake
  when server is in cached white-list
  once deployment is widespread (no need for white-list)
  Fall-back to SYN if no SYN-ACK-U
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U
SYN-ACK
SYN-ACK
SYN
RST
ACK
SYN-U
SYN-ACK
SYN-ACK-U
SYN
ACK
RST
-U = upgraded, i.e. magic no. at start of TCP Data
1
2
2
Cont...
Cont...
Upgraded Client
Upgraded Server
SYN-U
SYN-ACK-U
ACK
Cont...
1
3

## Slide 8: Inner Space – encapsulation model
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload

## Slide 9: Inner Space – applicability & compatibility*
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload
re: segment delivery
Timestamps
SACK
MPTCP Data ACK
re: stream delivery
tcpcrypt CRYPT
re connection
Max Segt Size
SACK-ok
Wnd Scale
Timestamp (1st)
TCP-AO
TCP Fast Open
tcpcrypt MAC
MPTCP (excl. DACK)
re: connection
Max Segt Size
SACK-ok
Wnd Scale
Timestamp (1st)
TCP-AO
TCP Fast Open
tcpcrypt MAC
MPTCP (excl. DACK)
* Many of the above schemes involve multiple different types of TCP option, see draft.

## Slide 10: middlebox domination strategy
long term aim
authenticate options
if turned on option authentication today
  ~10% of connections would break
  the ends break a working service
middlebox domination strategy
  Inner Space + option authentication (breaks 0%)
then, if middleboxes move into the TCP data
  the middleboxes break a working service
if you want to shoot them,
why shoot yourself in the foot
when you can make them shoot themselves in the foot?

## Slide 11: summary
make TCP options easy
  they will just work
  from the SYN onwards
next steps
review with a view to adoption
  focus: mandatory vs. optional elements
path testing
  data in SYN, is DPI bypass necessary? viable?
implementation
  compatibility testing
IAB workshop on stack evolution in a middlebox Internet
  principles

## Slide 13: menu
Problem (= summary of benefits)
Inner Space protocol
Applicability / compatibility
middlebox domination strategy
Next steps
Spare slides
Benefits & drawbacks
Tricky bits
Extensions

## Slide 14:  drawbacks - overheads
Dual Handshake Example
  Latency (Upgraded Server) Zero (Legacy Server) Worst of 2
  Connection Rate P*D 8%
  Connection State P*D/R 2.7%
  Network Traffic 2*H*P*D/J counting in bytes 0.03%
  2*P*D/K counting in packets 0.2%
  Processing {pending implementation} ?
Option on every non-empty segment
  Network Traffic P*Q*4/F 0.04%
  Processing {pending implementation} ?
Example
P : [0-100%] proportion of connections that use extra option space 80%
D : [0-100%] proportion of these that use dual handshake 10%
R : [round trips] ave. hold time of connection state 3
H : 88B for IPv4 or 108B for IPv6 (see draft for assumptions)
J : ave bytes per connection (in both directions) 50KiB
K : ave packets per connection (in both directions) 70 packets
Q : ave prop’n of InSpace connections that use it after handshake 10%
F : [B] ave frame size 750B

## Slide 15:  drawbacks - non-deterministic
the magic number approach traverses option stripping middleboxes, but...
probability that an Upgraded SYN or SYN/ACK is mistaken for an Ordinary Segment: Zero
probability that an Ordinary SYN or SYN/ACK with zero payload is mistaken for an Upgraded Segment: Zero
probability that payload data in an Ordinary SYN or SYN/ACK is mistaken for an Upgraded Segment: << 2-66 (roughly 1 connection collision globally every 40 years)

## Slide 16: disabling Inner Space temporarily
set Sent Payload Size (SPS) to special max value 0xFFFF
  sent segment was not 0xFFFF octets, but behave as if it was
  values above 0xFFE8 (= 216 – 25) are usable but not believable
regularly repeat just the 4B InSpace option
  every 0xFFFF octets (=44.7 * 1466B typical full-sized segments)

## Slide 17: tricky bits - zero payload segments
zero payload segments
  MAY include an Inner Option
  SHOULD NOT repeat the same Inner Options until more payload
other tricky bits  spare slides or draft
  option processing order
  options that alter byte-stream
    e.g. encrypt or compress
  the EchoCookie for SYN floods
  retransmissions during handshake
Without the ‘SHOULD NOT’ it would continue to ACK ACKs for ever

## Slide 18: tricky bits – option processing order
only on the first segment of each half-connection
  on later segments, Outer Options have to be processed before Inner
  reason: can’t find Inner Options if still waiting to fill a sequence gap
Base TCP header
Outer Options
InSpace Option
Prefix Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Sent Payload Size (SPS)
SYN=1
Magic A
1
SPS | InOO | Len
Magic Number B | SOO | CU
16b | 14b | 2b
Suffix Options Offset (SOO)
Suffix Options
Inner Options

## Slide 19: tricky bits – processing order: one level of recursion
If TCP alters the TCP Data (e.g. decrypt, decompress in the receiving case, for example)
  SYN=1: if it hasn’t previously found MagicA, it looks again
  SYN=0: There might be a rekey command in an encrypted Inner Option. So the TCP receiver decrypts up to the end of each set of Inner Options, processes those options, then continues decrypting (which might be with a new key).

## Slide 20: extension – DPI traversal
conjecture: DPI often parses payload & stops when it finds what it needs
solution?: locate MagicA at the end of the segment
  server searches for MagicA at end if not at start
can’t work from the end of every segment, only the first
  then use the spare first SPS (SPS#1) for the second segment
Base TCP header
Outer Options
SYN=1
InSpace Option#1
Inner Options
TCP Payload
Len=2
Inner Options Offset (InOO)
Magic A
1
Base TCP header
Outer Options
InSpace Option#2
Inner Options
TCP Payload
Len=1
Inner Options Offset (InOO)
SPS#2
first SYN=0
TCP Payload
SPS#1
DPI

## Slide 21: spare slides - to write, see draft
handshake retransmissions
explicit dual handshake
  corner cases of dual handshake
  deferred data in SYN

## Slide 22: Extensions – summary of dependencies
mandatory if implement Inner Space
  EchoCookie TCP option
extensions: optional while Inner Space is Experimental
    ModeSwitch TCP Option (scope wider than Inner Space)
    Explicit Dual Handshake (2 Outer TCP Options)
    Jumbo InSpace Option
    Inner Space segment structure for DPI traversal
DPI
see spare slides or draft

## Slide 23: Inner Space & TCP Fast Open (TFO)
If Upgraded Client uses TFO
  MUST place cookie in Inner of SYN-U
  then Legacy Server will not pass corrupt TCP Data to app before RST
If dual h/s, Upgraded Server will pass payload to app twice
  OK, because TFO only applicable if app immune to duplication
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U +InnerTFO
SYN-ACK
SYN-ACK
SYN+OuterTFO
RST
ACK
SYN-U +InnerTFO
SYN-ACK-U
SYN+OuterTFO
ACK
RST
-U = upgraded, i.e. magic no. etc. at start of TCP Data
SYN-ACK
App
App
1
2

## Slide 24: Inner Space & tcpcrypt
tcpcrypt capability negotiation currently adds a round trip
  not viable to add 1RTT delay to every connection to introduce opportunistic encryption
tcpcrypt currently attempts most of Inner Space
  in various complicated bespoke ways
  have proposed how to structure tcpcrypt over Inner Space
  cuts 1.5 rounds  makes tcpcrypt viable
  cuts out two states – greatly simplifies
  (?) decouples tcpcrypt from TCP state m/c
  tcpcrypt can encrypt Inner Options (incl. its own)
    because that needs reliable ordered delivery

## Slide 25: Inner Space & MPTCP
MPTCP adds Data ACK (in the DSS TCP Option)
  cumulative ACK of the set of sub-flows cannot be inferred
Data ACK is a per-segment message
  cannot use Inner Options
    would not be interpretable on reception (if out of order)
    potential deadlock: must not require receive buffer to ACK [1]
Three ways forward
  give up – leave all MPTCP TCP Options as Outer Options
  use Inner Space for a low latency MPTCP, except DSS and a way to test path for stripping DSS
  extend Inner Space to include Outer Options within TCP Data without using RWND or sequence space (hard – see next)
[1] Raiciu et al “How Hard Can It Be? Designing and Implementing a Deployable Multipath TCP”

## Slide 26: opportunities / further work
tcpcrypt-v2 decomposition
probes
  any Inner Options delivered reliably in order
relation to Minion, and multi-stream protocols
Outer Options in Inner for middlebox traversal
    without consuming rwnd (cf. fixed space for Outer Options)
    without consuming sequence space (avoiding middlebox ‘correction’)
    delivered immediately in received order, not sent order