## Slide 1: Tunnelling Through Inner Space
Bob Briscoe
Jan 2015
Bob Briscoe’s work is part-funded by the European Community under its Seventh Framework Programme through the Trilogy 2 (ICT-317756) and the RITE (ICT-317700) projects

## Slide 2: the old transport extensibility architecture
Source: The dataset collected for: Honda, M., Nishida, Y., Raiciu, C., Greenhalgh, A., Handley, M., and H. Tokuda, "Is it Still Possible to Extend TCP?", Proc. ACM Internet Measurement Conference (IMC'11) 181--192, Nov 2011
(nn): No. of paths tested to ea. port
Chart: port 34343 (unassigned)
| Cellular (20) | WiFi HotSpot (34) | Enterprise/SME (17) | University (17) | Home or Hosted (54)
port blocked | 0 | 0.058824 | 0.11765 | 0.17647 | 0
not proxied | 0.15 | 0.029412 | 0.058824 | 0 | 0
proxied | 0.05 | 0 | 0 | 0 | 0
Chart: port 443 (https)
| Cellular (20) | WiFi HotSpot (34) | Enterprise/SME (17) | University (17) | Home or Hosted (54)
not proxied | 0.15 | 0.029412 | 0.058824 | 0 | 0
proxied | 0.05 | 0.088235 | 0 | 0 | 0
Chart: port 80 (http)
| Cellular (20) | WiFi HotSpot (34) | Enterprise/SME (17) | University (17) | Home or Hosted (54)
not proxied | 0.1 | 0.029412 | 0.058824 | 0 | 0
proxied | 0.3 | 0.14706 | 0.11765 | 0.17647 | 0
Unknown option stripped from TCP SYN
0
4
8
12
16
20
24
28
32
36
40
( 4B) MSS
( 2B) SACK-ok
( 3B) WS
(10B) TS
(12B) MPTCP
(6-18B) TFO (shown as 12B)
(3B) CRYPT-hello
(bare min 84B) CRYPT-INIT-data
(3B) CRYPT-INIT
0
TCP SYN
TCP Data
TCP Option 'Space'

## Slide 3: Approach: Tunnel through Inner Space
Why should an implementation walk a list of extensions for which it has no code?
Extension can be coded to know where to look
[Rob Hancock re. IPv6 extensions (Trilogy project, Feb 2010)]
    options: layer X
    extensions: layer X+1 *
    end-2-middle: layer X
How to prevent legacy layer X passing corrupt payload to X+1?
Examples (see position paper):
  (L4) Minion
  (L4) Inner Space
  (L3) ConEx
  (L3) Generic UDP tunnelling (GUT)
IP
IP
IP
TCP
TCP
Middle-box
App
App
IP
Middle-box
TCP Header & Outer Options
Inner Options Within TCP Data
TCP Payload
Strawman principle: In a middlebox world, it is both more principled and more pragmatic to extend the layer X header within layer X+1 *
* In Internet arithmetic, 4+1 = 7

## Slide 4: Inner Space: in the TCP datastream
Control
Data
robust to resegmentation
Inner Options not prone to stripping
in-order delivery of Inner Options
out-of-order delivery also available
InSpace Option
Inner Options
TCP Payload
Magic No. A
InSpace Option
Inner Options
TCP Payload
InSpace Option
Inner Options
TCP Payload
TCP
TCP
Segmentation when Sent
Segmentation when Received
Sent Data Size (SDS) | Inner Options Offset (InOO) | Len
16b | 14b | 2b

## Slide 5: middlebox domination strategy
long term aim
authenticated control channel
if turned on option authentication today
  up to 40% of connections would break
  the ends break a working service
middlebox domination strategy
  Inner Space + option authentication (breaks 0%)
then, if middleboxes move into the TCP data
  the middleboxes break a working service
why shoot yourself in the foot
when you can make them shoot themselves in the foot?

## Slide 6: Inner Space: Implications & Status
Switchable transport semantics
  Looks like vanilla TCP on the wire
  switch inner semantics with TCP options e.g. ordering, encryption, compression
  think "extensible Minion"
Example: tcpcrypt decomposition
    cut from 18 to 9 CRYPT sub-options
    removed handshake latency
    can encrypt control options, and MAC pure ACKs
Progress since Jul'14
  Default mode: Full spec as individual draft (5 revs, presented in tcpm & tcpinc)
  TCPbis mode: Full spec available but not submitted <http://bobbriscoe.net/projects/2020comms/tcp/draft-briscoe-tcpm-inner-space-sink-00c.txt>
  ad hoc team formed (~20 people on mailing list)
  half-a-dozen doing or planning path traversal testing
  2 or 3 planning to implement, including upstreaming
Payload | Control Options |  | 
 | in-order | out-of-order | both
in-order | Default | (TCP) | TCPbis
out-of-order |  | (UDP) | UDPbis
both |  | (SCTP) | 'TCP2'
draft-briscoe-tcpm-inner-space-01
draft-briscoe-tcpm-inner-space-sink-00c
(splitting into sub-drafts - in progress)
Assessing whether 'TCP2' could satisfy HTTP2 reqs

## Slide 8: dual handshake... and migration to single
different source ports, same dest. port
no co-ordination needed between server threads
  can be physically separate replicas
Can use single SYN-U handshake
  when server is in cached white-list
  once deployment is widespread (no need for white-list)
  Fall-back to SYN if no SYN-ACK-U
Upgraded Client
Legacy Server Threads
Upgraded Client
Upgraded Server Threads
SYN-U
SYN-ACK
SYN-ACK
SYN
RST
ACK
SYN-U
SYN-ACK
SYN-ACK-U
SYN
ACK
RST
-U = upgraded, i.e. magic no. at start of TCP Data
1
2
2
Cont...
Cont...
Upgraded Client
Upgraded Server
SYN-U
SYN-ACK-U
ACK
Cont...
1
3

## Slide 9: TCPbis mode: 2 control channels in the datastream
00ZZ
InSpace Option
Suffix Options
TCP Payload
Magic
Suffix Options
TCP Payload
InSpace Option
TCP Payload
Prefix Options
00ZZ
InSpace Option
Suffix Options
Prefix Options
Control
Data
Out-of-Order
In-Order
Rcvr can reconstruct sent segments - robust to resegmentation
TCP has always processed Outer Options on arrival (out-of-order)
Inner Space adds two types of Inner Option to avoid middlebox interference
  In-order Suffix Options – for stream control
  Out-of-order Prefix Options
    essential for a few ACK-related options* to avoid flow-control deadlock
* SACK, MPTCP Data ACK, tcpcrypt MAC of ACK
Prefix Options
are processed on arrival
If this segment is delayed...
Suffix Options
wait