## Slide 1: L4S Architecture Low Latency, Low Loss, Scalable Throughput Internet Service
draft-briscoe-tsvwg-l4s-arch-00
B. Briscoe, K. De Schepper, M. Bagnulo
IETF97

## Slide 2: Motivation
Provide reduced latency for Internet traffic
Achieve that by reducing the queuing latency suffered by TCP packets.
  Current queues are inherent to the (large) saw tooth in TCP (either New Reno, Cubic or else)
  Proved (in closed environments) that transport protocols with small saw teeth can significantly reduce the queuing delays (DCTCP)
L4S aims to provide safe deployment of small teeth transport protocols in the Internet.

## Slide 3: L4S Architecture overview
Host
Protocol
Network

## Slide 4: L4S Architecture overview Host part - #3
Scalable congestion control already exists (DCTCP)
Additional mechanisms are needed to safe deployment in the Internet
  E.g. fall back to Reno if classic ECN bottleneck or in case of a loss, accurate ECN feedback
  See others in draft
Scalable congestion control for other transports

## Slide 5: L4S Architecture overview Network part #2
AQM that is able to isolate the L4S traffic from regular traffic
  If not L4s traffic would starve classic traffic and still not achieve low latency

## Slide 6: L4S Architecture overview Protocol part #1
A mean to distinguish L4S packets from regular packets, so the AQM can process them accordingly

## Slide 7: Status update
Source Code
  Dual Queue Coupled AQM, With Curvy RED for Linux (access available shortly), With PI2 for Linux [UPDATED]
  Data Centre TCP (DCTCP) fo Linux (in the mainline kernel), FreeBSD patch, ns2 patch.
  Accurate ECN TCP Feedback for Linux [COMPLETED, but not fully tested]
IETF specs
  Low Latency, Low Loss, Scalable Throughput (L4S) Internet Service: Architecture <draft-briscoe-tsvwg-l4s-arch> [NEW]
  A proposed new identifier for Low Latency, Low Loss, Scalable throughput (L4S) packets <draft-briscoe-tsvwg-ecn-l4s-id> [UPDATED to reflect the proposed process]
    enabled by <draft-black-tsvwg-ecn-experimentation> [NEW]
  Dual-queue AQM: : <draft-briscoe-tsvwg-aqm-dualq-coupled>
  scalable TCP algorithms, e.g. Data Centre TCP (DCTCP) <draft-ietf-tcpm-dctcp>
  Accurate ECN: <draft-ietf-tcpm-accurate-ecn> [UPDATED]
  Adding ECN to TCP control packets: <draft-bagnulo-tcpm-generalized-ecn> [UPDATED]
Papers
  Article in the IETF Journal describing the Demo in Bits-N-Bites at the IETF in Prague, July 2015. “Ultra-Low Delay for All” IETF Journal, Nov 2015.
  “Ultra-Low Delay for All: Live Experience, Live Analysis“, Proc. ACM Multimedia Systems; Demo Session (May 2016).
  “PI2: A Linearized AQM for both Classic and Scalable TCP,” Proc. ACM CONEXT 2016 (To appear Dec 2016). [NEW]

## Slide 8: Next steps
Please review and comment.
From the authors perspective, the document is in good enough shape for have a call for adoption.