## Slide 1: L4S TCP-Prague
ICCRG IETF98 Chicago
Koen De Schepper
Bob Briscoe
Olga Bondarenko
Inton Tsang

## Slide 2: DualQ for DCTCP
DualQ AQM was main focus up to now
Classic and DCTCP compatibility
PI2 as the classic AQM
Overload handling
Large number of experiments: flow numbers, RTTs, dynamic flows
L4S - DualQ concept proven, usable with DCTCP
3 drafts in adoption process in TSVWG
Release to Linux ongoing for DualPI2

## Slide 3: Now time for TCP-Prague
Internet-safety:
4.1: Fall back to Reno/Cubic congestion control on packet loss
4.2: Fall back to Reno/Cubic congestion control on classic ECN bottlenecks
4.3: Reduce RTT dependence
4.4: Scaling down the congestion window
tcpm: Accurate ECN and negotiation draft-ietf-tcpm-accurate-ecn
Performance improvements:
5.1: Setting ECT in SYN, SYN/ACK and pure ACK packets
5.2: Faster than additive increase
5.3: Faster convergence to fairness
implemented work in progress

## Slide 4: Prevent marking probability saturation
4.4: Scaling down the congestion window
Range p = [0 .. 1]
Range 1/p = [1 .. infinite]
Rate should range from [0 .. infinite]  1/p - 1
Solution: Average unmarked packets between marks
u = 1/p – 1 = (1-p) / p = q / p

## Slide 5: Average unmarked:
p = 10% 1/p = 10 u = 9 = 1/p – 1
p = 50% 1/p = 2 u = 1
p = 90% 1/p = 1,111 u = 0,111
avg( ) = 0,111
p = 100% 1/p = 1 u = 0
1
0
0
0
0
0
0
0
0

## Slide 6: Marking probability saturation
Drop based rate is also reduced by the dropped packets:
rdrop = (1 - p) / p.RTT
unified: r ~= u / RTT
Helps for
scaling the congestion window down
better drop compatibility
solving RTT independence

## Slide 7: Reduce RTT dependence
In Classic TCP, big queues  less RTT dependent:
  RTT1 = 100 ms + 20 ms queue delay = 120 ms
  RTT2 = 1 ms + 20 ms queue delay = 21 ms Rate ratio = 120/20 = 6x less throughput for flow with 100ms RTT
L4S has small or no queues at all  high RTT dependence
  RTT1 = 100 ms + 1 ms queue delay = 101 ms
  RTT2 = 1 ms + 1 ms queue delay = 2 ms Rate ratio = 101/2 = 50x less throughput for flow with 100ms RTT

## Slide 8: Marking rate & probability
Marking probability p
Equal for all flows
Used to converge to equal window or rate
Marking rate m = p.rate
Depends on the rate too
Is the signal frequency, which is indication for level of delay control

## Slide 9: Question for ICCRG
Compromise between:
RTT independence with RTTref = 2ms: r = 2 / p.RTTref = 1000 / p  p.r = 1000  always 1000 marks per second  not scalable to small RTTs
RTT scalability: r = 2 / p.RTT  p.r = 2 / RTT  always 2 marks per RTT  rate is very RTT dependent

## Slide 10: Where is the right compromise?
Current DCTCP: 2 marks per RTT
Less dependent: f(RTT) marks per RTT
The higher the RTT the more marks per RTT
Full RTT independence:
Constant marks per second (eg: 1 mark per ms)
The higher the rate the more marks per ms
Full RTT scalability and RTT independent:
Constant marking probability at all rates

RTT indep.
RTT scalable
rate converg.















## Slide 11: Where is the right compromise?
1
-1
m = marked packets per second = p * rate = f(RTTX, rateY)
0
1
-2
-1
Y = Exponent of rate
X = Exponent of RTT
Scalable
rate independent
m = f (RTTX)
Hyper-scalable
Non-scalable
RTT   rate 
RTT   rate 
Cubic
DCTCP
Reno
step
RTT independent: m = f (rateY)
p
RTT scalable: rate = f (RTT-1)

## Slide 12: Related DualQ discussion topics
L4S-only AQM:
DCTCP-like immediate step: p = 0 or 1; mark if p == 1
Gradual probability function: p = [0 .. 1]; mark if p > Random()
DualQ Coupling function:
Classic TCP-fairness is well known, but challenged: 1/sqrt(p)
Also coupling is determined by how DCTCP / TCP-Prague behaves
RTT-independent related coupling
work in progress
AQM
Priority scheduler
pC
L4S
Classic
qC
ECN
Classifier
mark
mark/drop
p²
>T
qL
&
pL
2p
ect(1), ce
ect(0), non-ect

## Slide 13: Conclusion
L4S - DualQ concept proven and usable with DCTCP
Low latency and low loss with window-fairness to classic Reno, Cubic, …
L4S: opportunity for new/existing improvements
What other improvements can we bring to the Internet together with L4S - DualQ?
Limited opportunity if tsvwg drafts go for last call
Think and discuss about RTT fairness
Next meeting in Prague: TCP-Prague implementations?