More Accurate ECN Feedback in TCP
draft-ietf-tcpm-accurate-ecn-03
Bob Briscoe <ietf@bobbriscoe.net>
Mirja Kühlewind <mirja.kuehlewind@tik.ee.ethz.ch>
Richard Scheffenegger <rscheff@gmx.at>

---
Problem (Recap)
Congestion Existence, not Extent
IP-ECN	Codepoint	Meaning
00	not-ECT	No ECN
10	ECT(0)	ECN-Capable Transport
01	ECT(1)
11	CE	Congestion Experienced
- Explicit Congestion Notification (ECN)
  - routers/switches mark more packets
    as load grows
  - RFC3168 added ECN to IP and TCP
- Problem with RFC3168 ECN feedback:
  - only one TCP feedback per RTT
  - rcvr repeats ECE flag for reliability, until sender's CWR flag acks it
  - suited TCP at the time – one congestion response per RTT
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...

---
Solution (recap)
Congestion extent, not just existence
- AccECN: Change to TCP wire protocol
  - Repeated count of CE packets (ACE) - essential
  - and CE bytes (AccECN Option) – supplementary
- Key to congestion control for low queuing delay
    - 0.5 ms (vs. 5-15 ms) over public Internet
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typ 5/8B, max 11B
TCP Options...

---
Where AccECN Fits
- Can only enable AccECN if both TCP endpoints support it (1)
    - but no dependency on network changes
- Extends the feedback part of TCP wire protocol
- Foundation for new sender-only changes (and for existing TCP), e.g.
  - congestion controls (TBA):
    - 'TCP Prague' for L4S (2)
    - BBR+ECN
  - Full benefit of ECN-capable TCP control packets (ECN++) (3)
  1. Backwards compatible handshake
    - SYN:	offer AccECN
      SYN-ACK can accept AccECN, ECN or non-ECN
  1. Low Latency Low Loss Scalable throughput [draft-ietf-tsvwg-l4s-arch]
  2. Without AccECN, benefit of ECN++ excluded from SYN [draft-ietf-tcpm-generalized-ecn]
TCP/IP
congestion control
(sender only)
Reno, Cubic, ...
Prague, BBR, ...
various CCs
transport
sublayers
TCP-AccECN
other transports
wire protocol
(both ends)
TCP-ECN
TCP
ECN++
IP

---
Recent Update – fall-back if bleached
   +--------+---------+------------+--------------+--------------------+
   | A | B | SYN A->B | SYN/ACK B->A | Feedback Mode |
   +--------+---------+------------+--------------+--------------------+
   | | | AE CWR ECE | AE CWR ECE | |
   | AccECN | AccECN | 1 1 1 | 0 1 0 | AccECN |
   | AccECN | AccECN | 1 1 1 | 1 1 0 | AccECN (CE on SYN) |
   | | | | | |
   | AccECN | Nonce | 1 1 1 | 1 0 1 | classic ECN |
   | AccECN | ECN | 1 1 1 | 0 0 1 | classic ECN |
   | AccECN | No ECN | 1 1 1 | 0 0 0 | Not ECN |
   | | | | | |
   | Nonce | AccECN | 0 1 1 | 0 0 1 | classic ECN |
   | ECN | AccECN | 0 1 1 | 0 0 1 | classic ECN |
   | No ECN | AccECN | 0 0 0 | 0 0 0 | Not ECN |
   | | | | | |
   | AccECN | Broken | 1 1 1 | 1 1 1 | Not ECN |
   | AccECN | AccECN+ | 1 1 1 | 0 1 1 | AccECN (CU) |
   | AccECN | AccECN+ | 1 1 1 | 1 0 0 | AccECN (CU) |
   +--------+---------+------------+--------------+--------------------+
- 2 unused handshake combinations (TCP ECN flags)
    - was: assume Non-ECN feedback
    - now: assume AccECN feedback
- Next rev: these are now needed to detect ECN bleaching
    - prevalent bug that wipes ECN – side effect of Diffserv bleaching
    - now that ECN++ is adopted (ECN on SYN)
      use these codepoints to feed back whether ECT(0/1) on SYN survived
- RFC3168 noted bleaching could happen, said it would be very bad,
  but silent on what to do about it (DISCUSS)

---
How Optional is the AccECN Option?
MUST NOT
- AccECN Option:
    - has to be implemented
    - MUST NOT include on SYN (not needed)(1)
    - SHOULD(2) include on SYN-ACK, ACK
      and first client data segment
- Note: never a “MUST”
  - but have to try
  - nonetheless, no-one can prove you didn't
    1. AccECN negotiation in flags implies AccECN Option support
    2. not if cached as black-hole path
SHOULD
SHOULD
SHOULD
Change-
triggered
&
OPTIONAL
(SACK takes
precedence
over space)

---
TCP NS flag → AE flag
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			AE	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
- NS flag
  - currently assigned to
    ECN Nonce [RFC3540] (EXP)
- Registry policy for TCP flags is “Standards Action” meaning “a Standards Track RFC”
- AccECN is EXPerimental track
- Process to make RFC3540 historic is in progress
  [draft-ietf-ecn-experimentation] (PS) Submitted to IESG for Publication
- Two additional steps needed (agreed betw WG chairs in AD Office hours):
  1. IANA unassigns NS → reserved.
     write into IANA section of ecn-experimentation
  2. IANA assignment as AE:
    1. accurate-ecn assigns flag to itself, which needs the IESG to agree to this process exception

---
Status & Next Steps
- Implemented in Linux(1)
- Been waiting for:
    - NS flag to become available
    - ECN++ to be adopted (see item (A) below)
https://github.com/mirjak/linux-accecn/
Open Design Alternatives (see Appendix B)
    1. Feed back all four ECN codepoints on the SYN/ACK (next rev)
    2. Feed back all four ECN codepoints on the First ACK (DISCUSS)
Open Issues (see Appendix C)
    1. Change-triggered ACKs: SHOULD or MUST? (DISCUSS)
    2. Is deliberate omission of AccECN Option a vulnerability?
    3. IANA Process
    - #2 can be left as part of the experiment
Then ready for final reviews and WGLC

---
AccECN
Q&A
spare slides

---
Recent Updates
- Recent updates that impact implementation:
    - S.3.1.1: Forward compatibility with two unused combination of flags on the SYN/ACK (see earlier slide)
    - S.3.1.2: Minor changes to cache management for SYN timeout fallback
    - S.3.2.2: Tighter test for first segment in either direction, when checking initial value of ACE
    - S.3.2.5: Tighter AccECN Option traversal tests
    - 3.2.5.5. Consistency between AccECN Feedback Fields