TCP Prague:
Resolving Tensions between Congestion Control Scaling Requirements
Supporting discussion paper:
https://riteproject.files.wordpress.com/2015/10/ccdi_tr.pdf
Bob Briscoe bobbriscoe.net
Koen De Schepper Nokia Bell Labs

---
Scaling congestion control dynamics
- whiskers: 1 standard deviation.
- %-age figures: resulting utilization of raw capacity
- 3G and 4G results captured over a production network [1]
- 5G Wide Area macro-cell results were simulated (next slide)
- Poor handling of dynamics by TCP's receive window was manually overridden
  in all cases (to focus on congestion control dynamics)
    - with autotuned rwnd and Cubic CC, 4G/LTE mean utilization was 43%

---
Why Such Poor Utilization?
- Right: video still of simulation to establish capacity dynamics
  - pedestrian mobility model
  - 3.5GHz macrocell (red) combined with 28GHz (blue) and 73 GHz (yellow) mmWave microcells
- Left: Goodput is for TCP Cubic over 20ms base RTT
  - each 10s grid line = 500 RTT
  - mean goodput: 1.2Gb/s; mean utilization: 19%

---
WiFi is no better
- 802.11ad
    - 60GHz 3Gb/s channel, static, office environment, occasional human blocking, Compound TCP
    - median goodput 280Mb/s, utilization 9.3%
    - near-perfect beam-forming improved utilization to 16% [2]

---
BDP = Bandwidth-Delay Product
Lesson from
design of high-BDP TCP protocols
- keep the number of round trips between drops small
- equivalently, keep the number of drops per round trip large
v : number of congestion signals per round trip
Cubic 800 Mb/s
v= 1/500
DCTCP any rate:
v = 2
DCTCP any rate
v = 2
Cubic 100 Mb/s
v=1/250
20ms round trips
250
500
750
1,000
1,250
1,500
1,750
2,000
W, window

---
v : number of congestion signals per round trip
W: congestion window
p: dropping or marking probability
Req#1. Scalable Congestion Signalling
- congestion signalling is scalable if v ≥ v0	(1)
  where v0 is a reasonable min
- v = (segments per RTT, W) * (probability each will be marked, p)
  v = Wp
  substitute in scalability constraint (1)
  W ≥ v0 / p	(2)
- can easily derive constraint on steady-state TCP equations from this...
  General congestion control formula:	,
- To satisfy (2), B ≥ 1
	B
Reno	½
Cubic	¾
DCTCP (prob. AQM)	1
DCTCP (step AQM)	2
{W} prop {1} over { p^{B}}

---
Approach to scaling the dynamics
- capacity decrease or other flows arrive: not the problem
- If capacity increases, or other flows depart, no information, except
    - ACK rate increases briefly while queue empties(1)
    - the next mark never comes...
- If normally 500 RTTs between marks, it takes ~1000 RTTs to notice their absence
- If normally 2 marks per RTT, it takes 1 RTT to notice
- Then sender can start probing for capacity
Goal: ultra-low standing queue;
The closer to our goal, the less we will detect this

---
Req#2: Limited RTT-dependence
- We have lived with this. Why change?
- Bufferbloat has cushioned us from the impact of RTT-dependent CC
- Low queuing delay
  leads large RTT
  flows to starve
  Note: this is an anti-starvation requirement not a strong 'fairness' requirement
E.g: base RTT ratio R1 /R2 = 200/2 = 100
	Qdelay / q	Total RTT imbalance (R1+q)/(R2+q)
Drop tail	200 ms	(200+200) (2+200)	≈ 2
PIE AQM	15 ms	(200+15) (2+15)	≈ 13
L4S AQM	500 μs	(200+0.5) (2+0.5)	≈ 80

---
Tension between Reqs 1 & 2
{pW} >= {v_0}{}newline{} {pW} prop {R}
- Scalable congestion signalling
- Limited RTT-dependence (pW/R const)
v : number of congestion signals per round trip
W: congestion window
p: dopping or marking probability
R: Total Round trip time

---
“Compromise 5” betw Reqs 1 & 2
- signals per RTT
  scalable signalling
  AND
  >>R0 RTT-independent
  <<R0 not RTT-dependent
- flow rate
{pW} = {v_0} over {lg(R_0/R + 1)}
{pW} over {R} = {v_0} over {R lg(R_0/R + 1)}
sorry for confusing you all: p ≈ 1/u

---
Resolving Tensions between
Congestion Control Scaling Requirements
6 scalability requirements (RTT, rate):
  1. Scalable congestion signaling
  2. Limited RTT-dependence
  1. Unlimited responsiveness
  2. Low relative queuing delay
  1. Unsaturated signaling
  2. Coexistence with Classic TCP
Link to paper:
     Resolving Tensions Between Congestion Control Scaling Requirements
https://riteproject.files.wordpress.com/2015/10/ccdi_tr.pdf
Link to experiment videos:
BBR with AQM: https://youtu.be/4eYfyKYe9nM
     BBR with Cubic: https://youtu.be/akO1HN2ey48
All links available via https://riteproject.eu/dctth/

---
more info
1. K. Liu and J. Y. B. Lee, "On Improving TCP Performance over Mobile Data Networks," IEEE Transactions on Mobile Computing, 2016.
2. Sur, S., Zhang, X., Ramanathan, P. & Chandra, R., "BeamSpy: Enabling Robust 60 GHz Links Under Blockage," In: 13th USENIX Symposium on Networked Systems Design and Implementation (NSDI 16) pp.193-206 (2016)