More Accurate ECN Feedback in TCP
draft-ietf-tcpm-accurate-ecn-04
Bob Briscoe, CableLabs
Mirja Kühlewind, ETH Zürich
Richard Scheffenegger, NetApp
IETF-100 Nov 2017

---
Problem (Recap)
Congestion Existence, not Extent
IP-ECN	Codepoint	Meaning
00	not-ECT	No ECN
10	ECT(0)	ECN-Capable Transport
01	ECT(1)
11	CE	Congestion Experienced
- Explicit Congestion Notification (ECN)
  - routers/switches mark more packets
    as load grows
  - RFC3168 added ECN to IP and TCP
- Problem with RFC3168 ECN feedback:
  - only one TCP feedback per RTT
  - rcvr repeats ECE flag for reliability, until sender's CWR flag acks it
  - suited TCP at the time – one congestion response per RTT
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...

---
Solution (recap)
Congestion extent, not just existence
- AccECN: Change to TCP wire protocol
  - Repeated count of CE packets (ACE) - essential
  - and CE bytes (AccECN Option) – supplementary
- Key to congestion control for low queuing delay
    - 0.5 ms (vs. 5-15 ms) over public Internet
- Applicability: (see spare slide)
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typ 5/8B, max 11B
TCP Options...

---
Fall-back if IP/ECN bleached/mangled
- We thought ECN traversal was surprisingly perfect
  ...until the latest measurement study*
    - ~60% of those mobile operators measured bleach upstream ECN by 1st IP hop
    - Prob. prevalent bug that wipes ECN as side effect of Diffserv bleaching
- Solution: Feed back (in the 3 TCP/ECN flags) which of 4 possible IP/ECN codepoints arrived on:
  - SYN	: in SYN-ACK
  - SYN/ACK	: in ACK of 3WHS
    - (With TFO, this ACK is not reliably delivered)
- If mangled, disable ECN for half connection
Octets 1-4 of
IPv4 header
* see ECN++ presentation (IETF-100 tcpm),
or http://www.it.uc3m.es/amandala/ecn++/
SYN
IP
ACK
IP
SYN/ACK
IP

---
Feedback of IP/ECN during 3WHS
1
   +--------+--------+------------+--------------+------------------------+
   | A | B | SYN A->B | SYN/ACK B->A | Feedback Mode |
   +--------+--------+------------+--------------+------------------------+
   | | | AE CWR ECE | AE CWR ECE | |
   | AccECN | AccECN | 1 1 1 | 0 1 0 | AccECN (Not-ECT on SYN)|
   | AccECN | AccECN | 1 1 1 | 0 1 1 | AccECN (ECT1 on SYN) |
   | AccECN | AccECN | 1 1 1 | 1 0 0 | AccECN (ECT0 on SYN) |
   | AccECN | AccECN | 1 1 1 | 1 1 0 | AccECN (CE on SYN) |
   | | | | | |
   | AccECN | Nonce | 1 1 1 | 1 0 1 | classic ECN |
   | AccECN | ECN | 1 1 1 | 0 0 1 | classic ECN |
   | AccECN | No ECN | 1 1 1 | 0 0 0 | Not ECN |
   : : : : : :
   | AccECN | Broken | 1 1 1 | 1 1 1 | Not ECN |
   +--------+--------+------------+--------------+------------------------+
1
Consumes last 2 combinations of
TCP/ECN flags on SYN/ACK
2
2
- Same coding on ACK
    - ACE counter in prev. drafts
  Notes:
  1. Could be TCP bleaching
  2. Used by RFC5562 + SYN cookie
  3. Currently Unused
   +--------------+---------------------------+------------------------+
   | ACE on ACK | IP-ECN codepoint on | Initial s.cep of |
   | of SYN/ACK | SYN/ACK inferred by | server in AccECN mode |
   | | server | |
   +--------------+---------------------------+------------------------+
   | 0b000 | {Notes 1, 2} | Disable ECN |
   | 0b001 | {Notes 2, 3} | 5 |
   | 0b010 | Not-ECT | 5 |
   | 0b011 | ECT(1) | 5 |
   | 0b100 | ECT(0) | 5 |
   | 0b101 | Currently Unused {Note 3} | 5 |
   | 0b110 | CE | 6 |
   | 0b111 | Currently Unused {Note 3} | 5 |
   +--------------+---------------------------+------------------------+
SYN
IP
ACK
IP
SYN/ACK
IP

---
Change Triggered ACKs
- SHOULD → “MUST with get-out clause”
- So that receiver can rely on the behaviour
    - e.g. at flow-start when heuristics waste valuable time
  “A concern has been raised that certain offload hardware needed for high performance might not be able to support change-triggered ACKs, although high performance protocols such as DCTCP successfully use change-triggered ACKs.
  One possible experimental compromise would be for the receiver to heuristically detect whether the sender is in slow-start, then to implement change-triggered ACKs in software while the sender is in slow-start, and offload to hardware otherwise.
  If the operator disables change-triggered ACKs, whether partially like this or otherwise, the operator will also be responsible for ensuring a co-ordinated sender algorithm is deployed;”

---
Minor Edits
- Clarified that AccECN is not dependent on ECN (of whatever flavour) in the network
- Experiment success criteria: added “deployed”
- Clarified that ‘Congestion Window Reduced’ signal is not used
- Defined behaviours for all unused values (forward compatibility)

---
Status & Next Steps
- Implemented in Linux(1)
- All open issues now closed
  - Appendix B “Alternative Design Choices” DELETED
  - Appendix C “Open Protocol Design Issues” DELETED
- Ready for WGLC
https://github.com/mirjak/linux-accecn

---
AccECN
Q&A
spare slides

---
Where AccECN Fits
- Can only enable AccECN if both TCP endpoints support it (1)
    - but no dependency on network changes
- Extends the feedback part of TCP wire protocol
- Foundation for new sender-only changes (and for existing TCP), e.g.
  - congestion controls (TBA):
    - 'TCP Prague' for L4S (2)
    - BBR+ECN
  - Full benefit of ECN-capable TCP control packets (ECN++) (3)
  1. Backwards compatible handshake
    - SYN:	offer AccECN
      SYN-ACK can accept AccECN, ECN or non-ECN
  1. Low Latency Low Loss Scalable throughput [draft-ietf-tsvwg-l4s-arch]
  2. Without AccECN, benefit of ECN++ excluded from SYN [draft-ietf-tcpm-generalized-ecn]
TCP/IP
congestion control
(sender only)
Reno, Cubic, ...
Prague, BBR, ...
various CCs
transport
sublayers
TCP-AccECN
other transports
wire protocol
(both ends)
TCP-ECN
TCP
ECN++
IP