Propagating ECN across IP tunnel Headers Separated by a Shim
draft-ietf-tsvwg-rfc6040update-shim-05
(posted this morning, sorry)
Bob Briscoe
bobbriscoe.net
IETF-100, Nov 2017

---
Problem #1
- RFC6040 “Tunnelling of ECN”;
  scope was all IP-in-IP tunnels
- rfc6040update-shim clarifies that scope of RFC6040 includes cases with shim
    - most feasible to propagate ECN if shim 'tightly coupled'
      (added in same step as IP outer)
- Standards track, so it can update standards track RFC6040 and shim tunnel RFCs
IPv4 or v6
IPv4 or v6
?
shim
L2
L2
IPv4 or v6
shim
shim
IPv4 or v6
IPv4 or v6
outer

---
Problem #2: unique to ECN
- Both Diffserv (traffic class) and ECN have to
  propagate across layers
  - DS propagates 'requirements' down
  - ECN propagates...
    - ECN field down (copy)
    - congestion experienced (CE) up
- forwarded ECN constructed from
  inner and outer on decap [RFC6040]
- If ECN decap behaviour absent,
  encap MUST zero ECN outer
app
L4
IPi
IPo
app
L4
IPi
IPo
app
L4
IPi
IPo

app
L4
IPi
IPo

CE
class
ECN
CE
ECN
zero

---
Survey of IP-shim-(L2)-IP encaps
Protocol	RFC	STDs or widely deployed	AOK	NOK: 6040shim updates		NOK: non-IETF: update recom’n’d
				Safe config	protocol
Geneve	nvo3-geneve		
GUE	intarea-gue		
SFC	7665		N/A?
VXLAN	7348					
VXLAN-GPE	nvo3-vxlan-gpe	
LISP	6830		
CAPWAP	5415		
Teredo	4380				
GTP	v1, v1U,v2C					
GRE	2784			
NVGRE	7637			
MIP4	5944				
MIP6	6275				
PMIP	5845				
L2TPv3	3931				
L2TPv2	2661				
PPTP	2637	
UDP	8085		
AMT	7450				
TCP+IKE/IPsec	8229		

---
Why update some protocols
but not others?
- In all cases, each base protocol RFC has been updated
  with an “operator safe configuration” clause
    - Places ref to ECN problem and solution in “Updated by” header
- Protocol Spec:
  if ( ( a maintainer of the protocol could be found)
    && (it seemed like code might get updated)
    && (I was confident I knew the implications of the update) )
    {I proposed fix to the control plane protocol, iterated, done}
  else
    {Am I bovvered?}

---
Updates to standards track tunnel RFCs
added this IETF cycle
- AMT (Automatic Multicast Tunnelling)
  - Updates to RFC 7450:
    - defined new flag on Request message for gateway to declare its ECN capability to the relay that will tunnel towards it (unidirectional)
    - Operator required to follow safe config in present spec
  - ACK: Jake Holland
- GRE (Generic Routing Encapsulation)
  - Update to RFC2784:
    - Operator required to follow safe config in present spec
  - Referred to (but not updated) 4 control protocols that are known to set up GRE tunnels
    - MIP4, MIP6, PMIP, IKEv2
  - ACK: Sri Gundavelli

---
Status and Next Steps
draft-ietf-tsvwg-rfc6040update-shim-05
- Rev posted this morning (sorry)
- Milestone: WGLC Sep 2017
- Been pushing to meet that,
  ready now - not so late
- Corridor chat this week might lead to updates to outstanding protocols (Teredo, (P)MIP)
    - Assume not

---
Propagating ECN across IP tunnel Headers Separated by a Shim
draft-ietf-tsvwg-rfc6040update-shim-05
Q&A

---
Compliance requirement for non-RFC6040 implementations!?
- Written as an operator config requirement
    - if decap does not, or might not, propagate ECN to RFC 6040 (or equiv),
      if possible, the operator MUST configure the ingress to zero the outer ECN field
- Prerequisite implementation requirement
    - Config of ECN encap MUST be independent from DSCP encap
- Added text updates RFC 6040, and shim tunnel RFCs
app
L4
IPi
IPo

app
L4
IPi
IPo

CE
ECN
zero