Low Latency Low Loss Scalable throughput (L4S) and RACK
– an opportunity to remove HoL blocking from links
Bob Briscoe, CableLabs	<ietf@bobbriscoe.net>
Koen De Schepper,	<koen.de_schepper@nokia.com>
TSVWG, IETF-103, Nov 2018
[Speaker Notes: Cover Slide 1 of 3 Cable Labs]

---
Recent ACKnowledgements (RACK): Background
- Loss is when sender deems absence has been long enough
    - Classic TCP:	3 DupACKs
    - TCP RACK:	a fraction (ε) of the RTT (termed the reordering window)
- Tradeoff – larger ε :
    - minimizes spurious retransmissions (before ACKs of reordered packets arrives)
    - but takes longer (1+ε)*RTT to repair genuine losses
- So, RACK adapts the reordering window:
    - starts small (which rapidly repairs losses in short flows)
    - then adapts to measured reordering degree
      (rapid loss repair less critical for performance of elephants)
- See draft-ietf-tcpm-rack-04
vs. delay
throughput efficiency

---
L4S Recap
- Motivation
    - Extremely low queuing delay for all Internet traffic, including link saturating
    - already 1-2 orders better than state of the art
    - 500 μs vs 5-15 ms (fq-CoDel or PIE)
- Architecture
Host
Protocol [ECN]
Network: DualQ Coupled AQM
1
3
2
L4S marker
 Scalable
sender
 L4S: [X1]
r ∝ {1} / {p}
1
p
ECN
Classifier
strict priority scheduler
Coupling
p2
Classic
sender
r ∝ {1} / {sqrt {p}}
Classic: [X0]
Classic drop or marking
r: packet rate
p: drop/mark probability

---
5th Requirement for L4S senders
- L4S 'TCP Prague' Requirements (for all transports protocols, not just TCP) draft-ietf-tsvwg-ecn-l4s-id-05#section-4.3
- to use ECT(1), a scalable congestion control:
    - MUST NOT detect loss in units of packets
    - rather, by counting in units of time
- Then link technologies that support L4S can
  remove head-of-line blocking delay
    - see Appendix A.1.7
like the TCP 3DupACK rule
like TCP RACK

---
Why the “MUST NOT”?
“to use ECT(1), a scalable congestion control MUST NOT detect loss in units of packets”
DualQ
Coupled
AQM
Disable
resequencing?
Default ECN classifiers
1
2

ECT(1)
CE
link
benefits
now
RACK only
 L4S
ECN
Classifier
Classic
link
benefits
in 30yrs?

Mix of RACK
and 3DupACK
Not-ECT
ECT(0)

---
Benefits of universal RACK to links (1/2)
- as well as e2e (layer-4) benefits,
  RACK offers potential for link (layer-2) performance improvements
- as flow rates scale up
  - with 3 DupACK rule
    - reordering tolerance
      time scales down
    - for multi-channel
      (bonded) links,
      skew tolerance time
      scales down
  - with rule relative to RTT
    - tolerance time
      remains constant
      (given min practical e2e RTT
      remains fairly constant)
e.g. RTT=24ms
3 DupACK
rule
3 DupACK
rule

12 pkts / RTT
6ms
750μs
96 pkts / RTT
multi-channel
(bonded) link

RACK adaptation range
RACK min, e.g. RTT/8

---
Benefits of universal RACK to links (2/2)
- for lossy links (e.g. radio)
  - with 3 DupACK rule
    - link rcvr buffers
      packets behind each gap
      while link re-xmts
    - head-of-line blocking
    - recall that packets on a link
      will be from different flows
      and different streams within flows
  - with rule relative to RTT
    - link rcvr can forward
      packets out of order
    - no reordering buffer
    - in parallel, link rexmt
      will typically fill gap within min
      RACK reordering window
fwd'ing
NACK
resequencing
buffer
retransmit
buffer
e.g. RTT=24ms
3 DupACK
rule
3 DupACK
rule

12 pkts / RTT
6ms
750μs
96 pkts / RTT

RACK adaptation range
RACK min, e.g. RTT/8

---
For discussion
- MUST NOT use packet counting at all
  (for L4S congestion controls)
    - is stricter than RACK
    - RACK starts with 3 DUP-ACK, then evolves to measured reordering window
- Starting with, say, RTT/8 would be an alternative
    - But at the start of a flow, SRTT is not (always) a good estimate
    - For TFO, might be completely wrong
    - But is it any more wrong than 3 DupACK?
- Discuss