More Accurate ECN Feedback in TCP
Bob Briscoe, Independent	<ietf@bobbriscoe.net>
Mirja Kuhlewind, ETHZ	<mirja.kuehlewind@tik.ee.ethz.ch>
Richard Scheffenegger, NetApp	<rs.ietf@gmx.at>
TCPM WG, IETF-106, Nov 2019
[Speaker Notes: Cover Slide 1 of 3 Cable Labs]

---
Problem (Recap): Congestion Existence, not Extent
IP-ECN	Codepoint	Meaning
00	not-ECT	No ECN
10	ECT(0)	ECN-Capable Transport
01	ECT(1)
11	CE	Congestion Experienced
- Explicit Congestion Notification (ECN)
    - routers/switches mark more packets as load grows
    - RFC3168 added ECN to IP and TCP
- Problem with RFC3168 ECN feedback:
    - only one TCP feedback per RTT
    - rcvr repeats ECE flag for reliability, until sender's CWR flag acks it
    - suited TCP at the time – one congestion response per RTT
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			NS	CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...

---
Solution (recap): Congestion Extent, not just Existence
- AccECN: Change to TCP wire protocol
    - Repeated count of CE packets (ACE) - essential
    - and CE bytes (AccECN Option) – supplementary
- Key to congestion control for low queuing delay
    - 0.5 ms (vs. 5-15 ms) over public Internet
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typ 5/8B, max 11B
TCP Options...

---
AccECN TCP Option Field Order
kind
length
EE0B [init=1]
ECEB [init=0]
EE1B [init=0]
kind
length
EE1B [init=0x800001]
ECEB [init=0]
EE0B [init=0]
- AccECN TCP Option
    - can omit fields that have not changed since the last ACK from the right hand end
- NEW?: Two types of AccECN TCP Options with the same kind
    - switch order of fields for whole connection
    - dependent on initial value of first field on first option received

---
Fixed inconsistencies
- Previously, WG made AccECN TCP Option optional
- Michael Scharf noticed that change-triggered ACKs text was inconsistent
    - said “...MUST send a change-triggered AccECN TCP Option...”
      - (a change-triggered ACK is an ACK that is triggered by change of a field)
    - made us realize we needed to describe change-triggered ACKs separately for the two cases:
        - ACE field only
        - ACE and AccECN TCP Option

---
Next Steps
- WGLC