More Accurate ECN Feedback in TCP
draft-ietf-tcpm-accurate-ecn-15
Bob Briscoe, Independent
Mirja Kühlewind, Ericsson
Richard Scheffenegger, NetApp
IETF-111 Jul 2021

---
Solution (recap)
Congestion extent, not just existence
- AccECN: Change to TCP wire protocol
  - Repeated count of CE packets (ACE) - essential
  - and CE bytes (AccECN Option) – supplementary
- Key to congestion control for low queuing delay
    - 0.5 ms (vs. 5-15 ms) over public Internet
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typ 5/8B, max 11B
TCP Options...

---
Implementation & Testing
- Linux v5.10 AccECN implementation [Ilpo]
    - https://github.com/L4STeam/linux
    - now works with all Congestion Control (CC) modules
      (Cubic, BBRv2, Prague, DCTCP, Reno, …)
    - enables A-B testing of CCs with consistent feedback code
- Also minimalist FreeBSD implementation (w/o TCP Option) of draft-09++ [RScheff]

---
AccECN and ACK Filtering
- Extensive testbed evaluation [Ilpo]. Ongoing
    - Wide area testing also needed
- Interim results compare the 4 degrees of feedback support shown
- Various traffic scenarios and AQMs
    - on-off (step) and spaced (probabilistic) ECN markings
- Built/building models of ACK filters
    - focus on worst-cases – up to 1/34 packets ACK'd, and not 'TCP-smart'
    - modelling closed source boxes is challenging
- Built/building simple heuristics for AccECN to fill the gaps
	AccECN TCP Option (3*24b)	ACE (3b)	DCTCP f/b (1b)		With ACK filtering
alwaysopt	Y	Y	-		As good as without filtering
minopt	Minimum	Y	-		As good as without filtering
noopt	-	Y	-		Usually good, some poor scenarios
dctcpfb	-	-	Y		Sometimes good, unpredictable

---
How often to ACK ACKs?
data
ACK
An AccECN Data Receiver:
    - SHOULD emit an ACK whenever a data packet marked CE arrives after the previous packet was not CE.
    - MUST emit an ACK once 'n' CE marks have arrived since the previous ACK..
- Intentions:
    - rapid feedback at congestion onset
    - reduce risk of double wrap of 3-bit ACE counter
- 2nd bullet could lead to ACKs of ACKs
  (first bullet deliberately doesn't)
    - 'OK in principle': ACKing new information (new CE marks)
    - to maintain cwnd during idles, or ready for adding ACK CC
    - 'n' no less than 3 to strongly damp potential ACK ping-pong
CE ACK
A
B
n	min	SHOULD	max
if newly delivered data to ack	-	2	6
if no newly delivered data to ack	3	3	6
time

---
Distinguishing ACKs of ACKs
from DupACKs
data
ACK
CE ACK
A
B
- ACKs of ACKs could be DupACKs [Yoshi]
    - if ACK stream CE marked
    - and data volleys take turns
- SHOULD implement extra DupACK test
    - not a DupACK if either is true:
      - SACK negotiated, but no SACK on the ACK
      - or using timestamps,
        and ACK sent before oldest unack'd data
- If extra test is not implemented
    - SHOULD NOT send ECN-capable pure ACKs
DupACK?
DupACK?

---
How often to ACK during a burst?
- If arrivals are processed as one burst
  (e.g. LRO/GRO)
- Does Receiver emit back-to-back ACKs? [Neal]
    1. every 'n' CE marks,
    2. every transition to CE?
- Guideline added:
    - both rules SHOULD be interpreted as requiring multiple ACKs to be emitted back-to-back (v similar to DCTCP)
    - If performance-critical, can emit one ACK at the end

---
AccECN TCP Option
Simplified Usage Rules
kind0
length
EE0B
[ECEB
[EE1B] ]
kind1
length
EE1B
[ECEB
[EE0B] ]
- When to include an Option (if using the Option at all)?
- SHOULD include option on every ack of newly delivered data
    - SHOULD include any counter field that ever changed
- Previously just guidance; now 2 SHOULDs, because:
    - You don't know which ACKs will survive ACK filtering
    - So, accurate and simple to include the Option on them all
- Removed requirements:
    - to beacon all fields
    - to emit an ACK when any byte counter changes
      (left in by accident after earlier edits)

---
Status & Next Steps
draft-ietf-tcpm-accurate-ecn-15
- Recent text tweaking
    - e.g. Transparent Middleboxes / TCP Normalizers [Gorry]
    - checked MUSTs with the eyes of a minimalist implementation
- Ready for WGLC, except
    - Waiting for SECDIR review
    - ACK filter testing ongoing
- draft-ietf-tcpm-generalized-ecn (EXP)
  dependent on this
- April’20 tcpm interim:
    - WG resolved to wait a while for L4S,
      but go ahead soon if still waiting

---
AccECN
Q&A
spare slides

---
Problem (Recap)
Congestion Existence, not Extent
IP-ECN	Codepoint	Meaning
00	not-ECT	No ECN
10	ECT(0)	ECN-Capable Transport
01	ECT(1)
11	CE	Congestion Experienced
- Explicit Congestion Notification (ECN)
  - routers/switches mark more packets
    as load grows
  - RFC3168 added ECN to IP and TCP
- Problem with RFC3168 ECN feedback:
  - only one TCP feedback per RTT
  - rcvr repeats ECE flag for reliability, until sender's CWR flag acks it
  - suited TCP at the time – one congestion response per RTT
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved				CWR	ECE	URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...